## Slide 1: SOP: Console Connection
Standard Procedure for Cisco & Aruba Devices
IT Department

## Slide 2: 1. Prerequisites - Hardware
• Network Device:
- Cisco Switch / Router
- Aruba Access Point / Controller
• Cables:
- RJ45 to USB Console Cable (Standard/Legacy)
- USB-C to USB-A Cable (Newer Devices)
• Computer:
- Laptop or PC with USB port

## Slide 3: 2. Prerequisites - Software
• Terminal Emulator:
- Windows: PuTTY, Tera Term, SecureCRT
- macOS: Terminal, Serial
• Drivers:
- Ensure FTDI or PL2303 drivers are installed.

## Slide 4: 3. Step A - Physical Connection
Scenario 1: Standard RJ45 Port
1. Locate port labeled 'CONSOLE' (Blue outline).
2. Plug RJ45 end into device.
3. Plug USB end into laptop.
Scenario 2: USB-C Port
1. Locate port with Wrench/Laptop icon.
2. Plug USB-C end into device.
3. Plug USB-A end into laptop.

## Slide 5: 4. Step B - Identify COM Port (Windows)
1. Right-click Start Button -> Device Manager.
2. Expand 'Ports (COM & LPT)'.
3. Look for 'USB Serial Port'.
4. Note the COM Number (e.g., COM3, COM4).
Note: If port is missing, reinstall cable drivers.

## Slide 6: 5. Step C - Terminal Configuration
• Open PuTTY (or equivalent)
• Connection Type: Serial
• Serial Line: [Your COM Port] (e.g., COM3)
• Speed (Baud): 9600
• Data bits: 8
• Stop bits: 1
• Parity: None
• Flow Control: None

## Slide 7: 6. Access & Troubleshooting
• Accessing CLI:
- Click 'Open'.
- Press 'Enter' until prompt appears (Switch>).
• Troubleshooting:
- Garbage Characters? Change Speed to 115200 (Aruba APs).
- No Response? Check power and correct 'Console' port.